### TriTester

### Model: TVLM-001

### Phase II Vapor Recovery

### Digital Rootsmeter Software

Version DR

August 1, 2008

##### OPERATING MANUAL

# Introduction

Thank you for purchasing TriTester, Triangle Environmental's Digital Rootsmeter Version DR software. The TriTester and DR software, are meant to be used in the place of the mechanical Rootsmeter to measure vapor volume. And can be used to test any system where you would use a mechanical Rootsmeter such as the VR 201/202 Healy Exhibit 5.

Additionally, the TriTester has met the requirements for use for conducting the Executive Orders VR-204, Vapor Systems Technologies, Inc. (VST), including Veeder-Root In-Station Diagnostics (ISD) System, Exhibit 11 test procedure.

Digital differences:

The TriTester and DR software, is meant to be used in the place of the mechanical Rootsmeter while following the test procedures with a few changes to improve the process and operate a digital meter.

Therefore you should follow the test procedure with the following general changes.

- When operating the TriTester with the DR software you will turn on the Tritester and select the DR option as it is available on the display screen by pressing the selector button.

- While following the test procedures press the selector button to zero out the meter before starting to pump the product for the test.

- After pumping the product, press the selector button again to display the readings.

- After the readings are recorded, press the selector button a third time to reset the meter for the next test.

Test Procedures

As examples, here are the specific additional steps for the Healy VR 201/202 Exhibit 5 and VST VR 204 test procedures.

Healy Section 7 Test Procedures:

7.2 Turn the TriTester on/off switch to the ON position, select Digital Rootsmeter software version, and press the selector button to zero the initial reading.

7.7.6 Press the selector button to read and record the final volume meter reading, in cubic feet.

VST Section 4 Test Procedures:

4.9

- Turn the TriTester on/off switch to the ON position,

- Select Digital Rootsmeter software version.

4.10

- Ensure the dispenser is not enabled to dispense product,

- Wait until the instruction screen displays the instruction to “Press start button to zero initial meter reading.”

- Then press the start button to zero initial reading.

- Record initial reading as zero on test data sheet “Start” value,

- Squeeze the nozzle handle to the full dispensing position,

- Turn the ball valve to the open position to allow nitrogen flow,

4.11

- Time flow for one (1) minute,

- Close ball valve to stop nitrogen flow,

- Release nozzle handle to the closed position,

- Press the start button to display TriTester DR “Stop” volume readings.

- Record the displayed values on the data sheet.

# Text boxes

Manufacturing, Inc.

Triangle